Interface Control Document of LCGT

| Subgroup Name | Vibration Isolation System |
| --- | --- |
| Subgroup Leader | Ryutaro Takahashi National Astronomical Observatory of Japan |
| Sub-leader | Takashi Uchiyama Institute for Cosmic Ray Research |
| Sub-leader | Shinji Miyoki Institute for Cosmic Ray Research |

| Doc version | Date | Description |
| --- | --- | --- |
| Rev. A-1 | 2009-08-25 | Reviced draft |

APPROVAL AUTHORITIES

Concise definition of vibration isolation system

System requirement

Displacement of the test mass mirrors must be less than 6x10-18m/Hz1/2 at 5Hz where the seismic noise and the radiation pressure noise are crossed. RMS motion must be less than 0.1m. The test mass mirrors are cooled to 20K through heat links.

SAS

Core optics are suspended by SASs. Two kinds of SASs are used in LCGT. Type-A SAS consists of an IP, three stage MGAS filters and a cryogenic mirror suspension. Type-B SAS consists of an IP, two stage MGAS filters and a mirror suspension. Type-A SASs are used for FM1, FM2, EM1 and EM2. Type-B SASs are used for BS, PRM, SEM, MC2F and MC2E.

Stack

Three stage stacks are used for BS, PRM, SEM, MC2F, MC2E, MC1F, MC1E, MMT and PD. Rubbers are enclosed by welded bellows. Some optics are placed on the stage 0.

Glossary

| SAS | Seismic Attenuation System |
| --- | --- |
| IP | Inverted Pendulum |
| MGAS | Monolithic Geometric Anti Spring |
| PF | Platform |
| IM | Intermediate Mass |
| MB | Magnet Box |
| TM | Test Mass |
| RM | Recoil Mass |
| ACC | Accelerometer |
| LVDT | Linear Variable Differential Transformer |
| FM | Front Mirror |
| EM | End Mirror |
| BS | Beam Splitter |
| PRM | Power Recycling Mirror |
| SEM | Signal Extraction Mirror |
| MC | Mode Cleaner |
| MMT | Mode Matching Telescope |
| PD | Photo Detector |

Figure: Schematic drawing of the vibration isolation system.

Table: Specification of the vibration isolation system

|  |  |  |  | # |  | Electric | Interface |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type-A SAS |  | 4 |  |  | Vacuum |
|  | Inverted pendulum (IP) |  |  |  |  |  |
|  |  | Leg | 30mHz | 3 |  |  |  |
|  |  | ACC | <10-10m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | LVDT | <10-8m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | Actuator | 10mm/V | 3 |  | DC15V | Control |
|  |  | Moter slider | ? | 3 |  | ? | Control |
|  | Filter0 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | Picomoter | ? | 1 |  | AC100V | Control |
|  | Filter1 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  | Filter2 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.5Hz, V: 0.2Hz | 1 |  |  |  |
|  | Platform (PF) | 120kg, 14K |  |  |  |  |
|  |  | mini-GAS | V: 0.7Hz | 4 |  |  |  |
|  |  | Picomoter | ? | 4 |  | AC100V | Control |
|  |  | Actuator | 1mm/V | 8 |  | DC15V | Control |
|  |  | Heat link | H: 14mHz, V: 8mHz, 1W |  |  |  | Cryostat |
|  | Intermediate mass (IM) | 60kg, 15K |  |  |  |  |
|  |  | Heat link | 1W |  |  |  | Cryostat |
|  | Magnet block (MB) | 60kg, 14K |  |  |  |  |
|  |  | Magnet | ? | ? |  |  |  |
|  | Test mass (TM) | 30kg, 20K |  |  |  | Optics |
|  | Recoil mass (RM) | 30kg, 15K |  |  |  |  |
|  |  | Actuator | ? | 4 |  | DC15V | Control |

|  |  |  |  | # |  | Electric | Interface |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Type-B SAS |  | 5 |  |  | Vacuum |
|  | Inverted pendulum (IP) |  |  |  |  |  |
|  |  | Leg | 30mHz | 3 |  |  |  |
|  |  | ACC | <10-10m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | LVDT | <10-8m/Hz1/2@1Hz | 3 |  | DC15V | Control |
|  |  | Actuator | 10mm/V | 3 |  | DC15V | Control |
|  |  | Moter slider | ? | 3 |  | ? | Control |
|  | Filter0 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  |  | Picomoter | ? | 1 |  | AC100V | Control |
|  | Filter1 | 120kg |  |  |  |  |
|  |  | MGAS | H: 0.55Hz, V: 0.2Hz | 1 |  |  |  |
|  | Platform (PF) | 120kg |  |  |  |  |
|  |  | mini-GAS | V: 2Hz | 4 |  |  |  |
|  |  | Picomoter | ? | 4 |  | AC100V | Control |
|  |  | Actuator | 1mm/V | 8 |  | DC15V | Control |
|  | Intermediate mass (IM) | 60kg |  |  |  |  |
|  | Magnet block (MB) | 60kg |  |  |  |  |
|  |  | Magnet | ? | ? |  |  |  |
|  | Test mass (TM) | 30kg |  |  |  | Optics |
|  | Recoil mass (RM) | 30kg |  |  |  |  |
|  |  | Actuator | ? | 4 |  | DC15V | Control |

| Stack |  | H: 2Hz | 9 |  |  | Vacuum |
| --- | --- | --- | --- | --- | --- | --- |
|  | Stage 0 |  |  |  |  |  |
|  |  | Breadboard |  | 1 |  |  |  |
|  |  | Bellows |  | 3 |  |  |  |
|  |  | Rubber |  | 3 |  |  |  |
|  | Stage 1 |  |  |  |  |  |
|  |  | Block |  | 3 |  |  |  |
|  |  | Bellows |  | 9 |  |  |  |
|  |  | Rubber |  | 9 |  |  |  |
|  | Stage 2 |  |  |  |  |  |
|  |  | Block |  | 3 |  |  |  |
|  |  | Bellows |  | 9 |  |  |  |
|  |  | Rubber |  | 9 |  |  |  |

| General requirement |  |  |  | Band | Interface |
| --- | --- | --- | --- | --- | --- |
|  | PSD displacement | 6x10-18m/Hz1/2 |  |  | 5Hz |  |
|  | RMS displacement | 0.1m |  |  | 0.1-4Hz | Control |
|  | RMS velocity | 0.1m/s |  |  | DC-4Hz | Control |
|  | RMS pitch | 10nrad? |  |  | 1-10Hz | Control |
|  | RMS pitch | 1rad? |  |  | 0.1-1Hz | Control |
|  | RMS yaw | 10nrad? |  |  | 1-10HZ | Control |
|  | RMS yaw | 1rad? |  |  | 0.1-1Hz | Control |