## Slide 1
Threshold:
Properties relating to the non-degenerate signal and idler fields are written with subscripts 1 and 2 respectively, and the pump field properties with subscript 3.
is the decay rate of the input coupler, is the decay rate of the output coupler,is the decay rate of the intra-cavity loss
h is Planck constant, c is light speed. The strength of the non-linear interaction is given by g which describes the rate at which photons transfer between fields and it is related to the waist in crystal[3].
[1]2012stefszky Thesis: Generation and Detection of Low-Frequency Squeezing for Gravitational-Wave Detection
[2]2018 Mansell G L Thesis :Squeezed light sources for current and future interferometric gravitational-wave detectors
[3]2016 Andrew Wade Thesis : Quantum limited measurements in gravitational wave
[4]2017 TT1700104-v2 aLIGO, SQZ, VOPO Cavity, Final Optical Design vopoFDD_v2
where Ri is the power reflectivity of the ith mirror. τ= L/c is the round trip time of the cavity. If the input coupler and output coupler are on the same mirror, then the Rout=1, then =0. L is the length of cavity.
Threshold
[1]
Reference:
[2]
If we want to calculate the threshold of VOPO, we need to know g and intra-cavity loss

## Slide 2
Intra-cavity loss:
According the reference[1], we can evaluate the Intra-cavity loss by the loss of each component in cavity:
For VOPO,
Rin1064=0.875
Rloss1064: 0.9985(M2 coating )*0.99992(M3,M4 HR coating)*0.9998(PPKTP absorption )* 0.9992(PPKTP AR coating) =0.996105 (loss1064=1-Rloss1064= 0.00389455)
Rin532=0.875
Rloss532: 0.9999(M2 coating )*0.99992(M3,M4 HR coating)*0.9998(PPKTP absorption )* 0.9952(PPKTP AR coating) = 0.98953 (loss532=1-Rloss532= 0.0104699)
These parameter are show in next page.
However, according to reference[1], this method for estimating the intra-cavity loss is very roughly.

## Slide 3
M1:
M2:
M3,M4:
Crystal absorption[1]
PPKTP coating:

## Slide 4
② Our VOPO is the same with LIGO-VOPO[4], so we can use their finesse in Table 1 and formula below to get the Intra-cavity loss
Finesse:
where Ri is the power reflectivity of the ith mirror. If the in coupler is the same with out coupler, then the Rout=1.
Rin1064=0.875
Finesse1064=46.1
Rin532=0.875
Finesse532=34.8
We can get: Rloss1064= 0.997267
Rloss532= 0.954127
[1]
According to[1,2], this method is more accuratly
[3]

## Slide 5
③ According to reference[2], we can measure the intra-cavity loss
where Pinc is the incident power and Pre f l is the reflected power.
when any mode mismatch or cavity misalignment, we need to subtract the high-order-mode power
where is the decay rate of the intra-cavity loss
where Ri is the power reflectivity of the ith mirror.
Input/output coupler
τ= L/c where τ is the round trip time of the cavity

## Slide 6
VOPO 532nm reflected signal: Pinc=4.70mW , Prefl=4.59mW
R532 loss= 0.99921,Finesse 532= 46.7684(34.8)
VOPO 1064nm reflected signal: Pinc=4.72mW , Prefl=4.66mW
R1064 loss= 0.999545, Finesse 1064= 46.8854(46.1)
High-order-mode/(High-order-mode+Main-mode)=0.061955
0.2887mW

## Slide 7
The strength of the non-linear interaction g:
According to the reference [1,3], the g is related to the waist in the crystal. Our VOPO’s waist in crystal is the almost the same with reference[3], so we can use g=1016(1/s).
 | PPKTP Length(mm) | Cavity Length(m) | Reflectivity of Mir | Waist of Cavity in crystal(μm) 532nm | Radius of M3,M4(mm) | g
Our VOPO | 10.7 | 0.344 | R1=0.875(0.875) R2=0.9985(0.999) R3=R4=0.9999(0.9999) | 21 | -50 | 1016
[1] | 10.5 | 0.273 | R1=0.839(0.722) R2=0.9985(0.9985) R3=R4=0.999(0.999) | 23.01 | -38 | 1891
[3] | 10.5 | 0.345 | R1=0.845(0.7) R2=0.9985(0.9985) R3=R4=0.9999(0.9999) | 21.2 | -50 | 1016

## Slide 8
Summary
Using the formula:
Substitute the non-linear interaction strength g=1016(s-1) and Rin=87.5%, Rloss into it
We can get the threshold:
τ= L/c
where
L is the length of cavity
in our case
Ri is the power reflectivity of the ith mirror
1=1064nm
3=532nm
 | Component specs | LIGO’s parameter | Experiment measurement | 
Finesse | 43.6067 45.7088 | 34.8 46.1 | 46.8 46.9 | 17 36
Threshold(mW) | 44 | 68 | 36.1 | Haven’t finish
Oscilloscope