## Slide 1
K.Somiya
Gravitational-wave detectors
The 3rd Thermal Noise Workshop at Jena
July 2015
Tokyo Inst of Technology
Kentaro Somiya

## Slide 2: What is a gravitational wave?

## Slide 3: Gravitational waves
Newton’s gravity
“attracting force btw apple and earth”
Einstein’s gravity
“free fall in a curved space-time”
“Dynamic change of the space-time
will propagate as a wave”
Prediction of GW
by Einstein
(1916)

## Slide 4: Effect of gravitational waves
+ mode
x mode
Distance of 2 objects shrinks in one direction and
expands in the other direction.

## Slide 5: Interferometric GW detector
Laser
Expand
Shrink
Photo-
detector
Supernova explosion,
Black hole binaries, etc.
Gravitational Waves
Massive Astronomical events
Distance of two objects changes
Observe the change with
big high-power interferometers
Far Galaxy
Earth
LIGO in US [4km]
Virgo in Italy [3km]
GEO in Germany [600m]
KAGRA in Japan [3km]

## Slide 6: What can we learn from GW?

## Slide 7
[CG: NASA]
[image: Hubble]
Black Hole
Quasi-normal mode
Supernovae

## Slide 8
[image: NASA]
Early Universe

## Slide 9
GW
Supernova
Blackhole
Neutron Star Binary
Cosmic
Background
Pulsar
Unknown
Nuclear
Physics
Astronomy
Cosmology
Relativity

## Slide 10: GW in books about time-machine
Kip Thorne’s time-machine using a warm hole
[Phys Rev Lett 1988]
Reference
Time-machine study requires more knowledge on Quantum Gravity, and GW observation is the way to understand Quantum Gravity.
Kip Thorne

## Slide 11: GW observation history

## Slide 12
1969 Weber

## Slide 13
1974 Hulse & Taylor
(1993 Novel Prize)

## Slide 14
1970's Interferometric GW detector

## Slide 15
2002 LIGO(US) started observation
2005 GEO(GER/UK) started observation
2007 Virgo(ITA/FRA) started observation
1999 TAMA(Japan) started observation

## Slide 16
Virgo
GEO
TAMA
LIGO
LIGO
Global GW observation network

## Slide 17
2010 News:Discovery of GW!?

## Slide 18: 1G detectors observed up to 70M LY, but no GW signal was found Upgrade to higher-sensitivity 2G detectors

## Slide 19: Sensitivity of 1G detectors
LIGO
Virgo
Sensitivity is limited by
(i)seismic noise (ii)thermal noise (iii)quantum noise
Strain of 10-23
(~10-19m/rtHz)

## Slide 20
Seismic
Solutions
Isolation
Underground
Feedforward

## Slide 21
Thermal
Solutions
Material
Cryogenic
Large beam
Beam shape
Mirror shape

## Slide 22
Quantum
Photon-number
fluctuation
Solutions
High power
Resonator
Squeezing

## Slide 23: Second generation detectors
KAGRA
Virgo
GEO
TAMA
LIGO
LIGO
LIGO
Virgo
GEO
upgrade
Advanced LIGO
Advanced Virgo
GEO-HF

## Slide 24
Advanced LIGO

## Slide 25
Advanced Virgo

## Slide 26
GEO-HF

## Slide 27
KAGRA
223mm
153mm

## Slide 28: Comparison of Advanced LIGO and KAGRA
KAGRA
Advanced LIGO
Heisenberg
Limit (23kg)
 | KAGRA | Advanced LIGO
Temperature | 20K | 290K
Test masses | 23kg Sapphire | 40kg Silica
Limiting noise | Quantum | Coating thermal
Configuration | Detuned RSE | Broadband RSE
Circulating power | 250-400kW | 800kW
Heisenberg
Limit (40kg)

## Slide 29: Detuning and optical spring
Nl
detune
Locked to a detuned position from resonance
Go far from reso >> less RP
Come close to reso >> more RP
Optical Spring!
Spring
Laser
With the optical spring, the sensitivity can exceed the
Heisenberg's Standard Quantum Limit (SQL)

## Slide 30: Coating thermal noise
Advanced LIGO is in the room temperature
Thickness cannot be changed much for high reflectivity
Poisson ratio being 0.5 means extreme softness
Young's modulus represents the hardness (of the mirror)
LIGO has been trying to reduce f and increase w
Power spectrum of coating TN (the simplest form)
T: Temperature, n: Poisson ratio,
d: coating thickness, Y: Young's modulus,
w: beam radius, f: mechanical loss

## Slide 31: What will happen in the near future?

## Slide 32
2018 First detection of GW
aLIGO's project term is till 2018 and
it has to realize the first detection.
The prospect is
10% for the detection in '15 (O1)
50% for the detection in '16-17 (O2).
No GW in O2 -> O3 in '18
GW in O2 -> Major upgrade in '17-18
Ad-Virgo is trying to join from O2.
KAGRA is trying to join from O3.
If we see no GW in O3, it will mean that the theory
must be wrong.

## Slide 33
2020 GW astronomy
Del Pozzo et al, PRL (2013)
With all the detectors in operation at the design sensitivities,
we will see multiple events per year to find new Physics.

## Slide 34
2020 Space detector projects back
LISA has been stopped in the US but
there is a chance to restart the project
if the first detection happens by '17.
eLISA in Europe: plan to launch in '45
LISA in US: aiming at launch in '25

## Slide 35
2020~ Einstein Telescope and Cosmic Explorer
ET in Europe
- Consists of two detectors
(high-power HF and cryo LF)
- 10km triangle
- Underground
CE in the US
- 290K Single detector
- 40km (probably triangle)
- On-ground
3G detectors may share a single global project
The first joint workshop is held in 2015 Feb.

## Slide 36: Comparison of KAGRA and ET-LF
 | KAGRA | ET-LF
Temperature | 20K | 10-20K
Test masses | 23kg Sapphire | 120-200kg Silicon
Configuration | Detuned RSE | Detuned RSE with squeezing
Circulating power | 250-400kW | ~20kW
wavelength | 1064nm | 1550nm
Arm length | 3km (underground) | 10km (underground)
KAGRA and ET-LF have many in common.
ET-LF has solved some of the problems in KAGRA.
Large crystal is available for Silicon
Low-power operation eases the heat extraction
One problem that remains is the absorption of a large Silicon.

## Slide 37: Current status of KAGRA

## Slide 38: KAGRA is in Kamioka

## Slide 39: Inside the mine
Nissan's electric car
Electric
bike
Bicycle

## Slide 40: Installation works
Installation of a stack system
External view of the Laser room
Cryostat installation

## Slide 41: KAGRA's cryogenic system
[Heat flow]
laser -> Sapphire mirror -> Sapphire fiber
-> Al heat link -> shield -> cryo-cooler
Toshiba factory in Yokohama
Sapphire test masses are cooled down to 20K

## Slide 42: Cryogenic suspension
ear
nailhead
Indium
bonding
Sapphire
blade spring
Mirror side will be cut
and polished for HCB.
Various tests have been done.

## Slide 43: Sapphire test mass
Absorption and refraction index maps of the Sapphire path-finder
Influence of the inhomogeneity
is to be simulated.
absorption inside 100mm aperture | S1 [ppm/cm] | S2 [ppm/cm] | S3 [ppm/cm]
#1 (F62-22) | 40.7 | 63.5 | 62.7
#2 (F47-21) | 69.4 | 84.0 | 91.2
#3 (AC-179) | 55.6 | 34.0 | 48.7
#4 (F39-56) | 85.3 | 334.9 | 148.3
Absorption of four test masses that have been delivered
S1
S3
S2
#3 has bubbles.

## Slide 44: Summary
Second-generation GW detectors are to start
the operation and to realize the first detection
Third-generation GW detectors have started
the design study and can share a single design
KAGRA and ET-LF have some techniques in
common and have been collaborating under ELiTES

## Slide 46: Coating thermal noise
Advanced LIGO is in the room temperature
Thickness cannot be changed much for high reflectivity
Poisson ratio being 0.5 means extreme softness
Young's modulus represents the hardness (of the mirror)
LIGO has been trying to reduce f and increase w
Power spectrum of coating TN (actual form)
T: Temperature, n: Poisson ratio,
d: coating thickness, Y: Young's modulus,
w: beam radius, f: mechanical loss
Sapphire Y=4.0e11, nu=0.23
Silica Y=7.2e10, nu=0.17
Silicon Y=1.3e11, nu=0.22
Tantala Y=1.4e10, nu=0.23

## Slide 47: Frequency-dependent squeezing in KAGRA
FD squeezing effectively increases laser power & mass.
With 6dB FD SQ, KAGA BNS obs range will be ~200Mpc.